## Slide 1: Emerging Technology Meetup # 3: The Internet of things (IoT)
Date: 2/1/2019

## Slide 2: Timeline
45 minutes
Motivations and the Digital Twin
10 minutes
15 minutes
INTRO
PRACTICE w/ AZURE IoT
1 Simulated Device
Multiple Devices, Adding 1 physical device
Machine Learning Challenge
20 minutes
DATABRICKS
TOTAL: 1.5 hrs.

## Slide 3: Motivations
Devices are becoming ubiquitous
  Autonomous vehicles, home automation and security, healthcare, wearable tech
The application development rate is rapidly increasing
  4 Major, Cloud-Based IoT Hubs (and another dozen second-tier hubs)
  >4000 Node-Red Device Flows
  Major IoT systems deployments underway
Vehicle technology is pushing the envelope
  Autonomous vehicles
    V2V, V2I, V2P (V2X)
On top of all that … there is a convergence of technologies
  IoT – data generation
  Big Data – data storage and analysis
  AI/Machine Learning – predictive analytics and control
  Blockchain – ecosystems of intelligent agents
https://www.youtube.com/watch?v=QSIPNhOiMoE
We don’t need a Gartner report to see that…

## Slide 4
Internet of Things Landscape 2018

## Slide 5: Examples of IoT
Just Walk Out – Amazon Go
  https://www.youtube.com/watch?v=NrmMk1Myrxc (1:49)
Rio Tinto - Driverless Train
  https://www.youtube.com/watch?v=8A-GAg69rAM (3:24)
  Moving Block/Communications-Based Train Control (CBTC)
    https://www.youtube.com/watch?v=_1Bgmugve5M (2:11)
Microsoft – Integrating Wearable Health Tech
  https://www.youtube.com/watch?v=u5oTz1e5qqE (14:30)
Driverless Vehicles
  https://www.youtube.com/watch?v=gfWjsKsEry0 (5:04 – Autonomous Taxi)
  https://www.youtube.com/watch?v=Qb0Kzb3haK8 (2:33 – Autonomous Truck)
  https://www.youtube.com/watch?v=L_uW0_OvEkk (6:55 – Motivation for Autonomous Trucking)
  https://www.youtube.com/watch?v=gD3gXblRhC4 (3:04 – Volvo Platooning/DSRC)
  https://www.youtube.com/watch?v=OdhzRJQ7Qfw (3:49 – Logging Operations Platooning/DSRC)
  Ford Announced V2X Technology in all Vehicles @ CES 2019
Integration with GIS
  https://www.arcgis.com/apps/MapJournal/index.html?appid=895bd00c9e7c4521b21e94da5d4748fc#

## Slide 6: Historical Background
Process Automation – Sensing and Control
  Utilities
  Industrial Processing
  Vehicle electronics
  Aircraft
Black Box Perspective
  Nobody wants/needs to know about how, e.g. power company checks meters
  Protocols/Networks were competitive advantage
  Only specialists would need to know
Specialized Languages, Methods, Hardware
  Supervisory Control And Data Acquisition (SCADA)
    Ladder/Flow Programming (IDE), HMI’s, Data Storage,
  Programmable Logic Controllers (PLC)
    Logic downloaded from SCADA
    Monitored by SCADA
  Both Proprietary and Open Network Protocols, e.g. Modbus (request/response messaging)
  Industry 4.0 = SCADA + IoT
OPERATIONAL
TECHNOLOGY
INFORMATION
TECHNOLOGY
ERP (ledgers, CMMS, supply chain)

## Slide 7: Historical Background, cont.
First Wave of Disruption
  Personal Computing
    Personal weather stations
    Home automation/Security
    Personal electronics, e.g. Bluetooth devices
Second Wave of Disruption
  Cloud-based Integration
    Devices became cloud-enabled, e.g. Arlo security cameras
  Control Needed to be Personalized
    Systems of devices needed to be plug-n-play, e.g. smart home control
OPERATIONAL
TECHNOLOGY
INFORMATION
TECHNOLOGY
ERP (ledgers, CMMS, supply chain)

## Slide 8: Disruption: Merging OT and IT
Control Engineering (evolution)
  Gen1: Monolithic
  Gen2: Distributed (LAN)
  Gen3: Networked - Process Control Network (PCN)
  Gen4: IIoT – Multi-protocol, Edge, Gateway, Cloud
Security “out of focus” through Gen 2
  Server Message Block (SMB) – WannaCry (EternalBlue SMB Exploit)
  https://en.Wikipedia.org/wiki/The_Shadow_Brokers
Request/Response Messaging
Low Level Languages
  (Relay) Ladder/Flow
  A cautionary tale - http://engineeredtruth.com/why-i-have-left-the-plc-programming-field/
Software Engineering
  Scalable, distributed computing
  Cloud-based storage
  IoT Networks
    Mesh/Edge/Gateway/Cloud
  Availability of complex control paradigms, machine learning, intelligent agents
Security Emphasized
Publish/Subscribe Messaging
Multiple High Level Languages
  C#, JS, etc.
Honeywell, Rockwell Automation, Allen-Bradley, Siemens (becoming IIoT)
Google, Microsoft, AWS, IBM, Device Manufacturers (IoT & IIoT)
TODAY

## Slide 9: OT Security Paranoia? Think again…
“It’s a golden age to be an attacker against critical infrastructure. If you are in critical infrastructure you should plan to be targeted. And if you are targeted, you will be compromised. It’s that simple.”
Andy Bochman, Senior Grid Strategist for National & Homeland Security at the Idaho National Laboratory (INL)
Shadow Brokers code release was to be seen as a warning: "Retaliate for the D.N.C., and there are a lot more secrets, from the hackings of the State Department, the White House and the Pentagon, that might be spilled as well. One senior official compared it to the scene in The Godfather where the head of a favorite horse is left in a bed, as a warning."

## Slide 10: Acronymn Soup: Protocols and Data Formats
Promising Protocols, Architectures and Standards
  Must support addressing, low power, limited data
    CoAP/UDP/IPV6/802.15.4 - Constrained Application Protocol
    6LoWPAN – IPV6, low power, wireless, personal area network
  Emerging reference architectures
  Virtually all Cloud-based IoT Hubs implement - Message Queue Telemetry Transport (MQTT) – lightweight pub/sub
Promising Data Formats
  Typically JSON over MQTT
  https://developers.google.com/protocol-buffers/
  Vehicle Safety Specific – DSRC/JSON over WSMP
CAV Specific Network
  Wireless Access in Vehicular Environments (WAVE) – 802.11p, J2735

## Slide 11: IoT (Hubs) Cloud Gateways on the Scene
Developing the IoT Model: the Generic (Gateway) Hub Approach
  AWS IoT
  IBM Watson IoT
  Google IoT
  Azure IoT
Device Definition
  Device Provisioning
  Digital Twin (aka Device/Shadow/Virtual Twin) – Virtualization of the Physical Device
Data Streams
  Ingestion, Storage, and Learning
  Focus on serialization/deserialization (aka marshalling)
Integrated Development/Provisioning Environments
  AWS IoT
  IBM Watson - Node Red
  Google IoT Core
  Azure IoT

## Slide 12: IoT Hubs: Reference Architecture(s)
IOT (GATEWAY) HUB
EDGE HUB
CLOUD SERVICES, APPLICATIONS
&
DIGITAL TWINS
CLOUD ANALYTICS
(ML PIPELINES)
STREAMING
DATA
ML MODELS
DATA STORAGE
Zigbee
Wi-FI
Bluetooth
DEVICES
TM
RM
RM
RM
1. PREPARE
2. DECIDE
3. COMMIT
1. PREPARE
2. DECIDE
3. COMMIT
1. PREPARE
2. DECIDE
3. COMMIT
4. COMPLETE
DATA
CONTROL PROVISION CONFIG

## Slide 13: Reference Architectures
IIoT/Process Automation
  https://cloud.google.com/solutions/iot/
  https://www.researchgate.net/publication/328007992_Practical_Guide_to_Smart_Factory_Transition_using_IoT_Big_Data_and_Edge_Analytics
  https://docs.microsoft.com/en-us/azure/iot-edge/iot-edge-as-gateway
IoT Cloud/Edge

## Slide 14: Digital Twin
Definition: Digital replication of a physical asset
  People, place, device, or system
  Implemented as objects, e.g. JSON in Azure
Provides Properties and Settings (over life cycle)
  Properties = meta-data, e.g. serialNumber
  Settings = setpoints, e.g. targetTemperature
Functional areas
  Provisioning
  Persisting Device Data
    Manufacturer, Serial Number
  Handling device settings
    Updating based on user input, e.g. new targetTemperature
  Controlling Behavior
    Indicating desired settings, e.g. comparing desired to required
  Releasing new control software, e.g. a newly learned model
  Consuming Predictive Analytics Results
  Scheduling Preventive and Predictive Maintenance
I’m getting an overhaul!
Here comes telemetry data!
I’ll control, connect, and provision!
PERFORMANCE DATA
WORK ORDERS
SETTINGS DATA
Time to prioritize and schedule
Digital Twins
Analytics Services

## Slide 15: Digital Twins: examples
Facilities
https://vimeo.com/304911148?from=outro-embed
https://cityzenith.com/smartworldpro/digital-twin-solutions/
Industrial Processing
https://www.ge.com/digital/sites/default/files/download_assets/Digital-Twin-for-the-digital-power-plant-.pdf
Government
https://www.govloop.com/community/blog/future-now-3d-digital-twin-government/
Software Environments
https://www.scaleoutsoftware.com/products/digital-twin-builder/?gclid=EAIaIQobChMI6aKA8fyV4AIVj4rICh3esAduEAMYAyAAEgJ8XfD_BwE

## Slide 16: Digital Twin: cont.
Sending telemetry data to the IoT hub
Caching telemetry data to persistent storage, e.g. the event hub or DB.
Performing machine learning, i.e. executing a pipeline to generate a model
Digital Twin is typically not:
Offloads non-telemetry/control task behaviors
Manages the life cycle of the device
Stores meta-data about the device
Enables background improvement, e.g. learning
What’s great about the digital twin?

## Slide 17: Digital Twin: Provisioning
Bootstrapping
getting ID/metadata
Credentialing – secure authenticated communications
Acquiring a token
Authorization – acquire persmissions
Permission + Credential  Resources
Connecting
Establishing network connectivity
Registration
Being known to other resources

## Slide 18: Convergence with Emerging Tech
Big Data
Streaming IoT data often results in large datasets
Learning in both real-time (streaming) and off-line (batch) modes
Learning opportunities for predictive analytics (graceful failures, pre-emptive repair) and control (adapting to machine usage)
Blockchain
Devices are typically part of an ecosystem
Ecosystem might include transactions, e.g. paying for usage
  Smart Contracts provide business logic layer
Log data for private usage should be both private and secure (audits)

## Slide 19: Demonstrations
Remote Monitoring
Simulated Devices
Telemetry to Dashboard
Using Time Series Insights
Data Analytics
Event Hubs Data Capture
Databricks Evaluation

## Slide 20: Next Steps: Meetup Challenge
Pick a domain
  Environmental Monitoring
  Freight Movement
  Waste Water Treatment
Propose something to learn from your data
See your machine learn at the next meetup!
Big Data from IoT is just a lot of data…without Machine Learning!

## Slide 21: Picking a ML Paradigm